## Slide 1: Attestation Results for Connectivity
Eric Voit
Cisco
evoit@cisco.com
draft-voit-rats-attestation-results
Henk Birkholz Fraunhofer SIT
henk.birkholz@sit.fraunhofer.de
Thomas Hardjono
MIT
hardjono@mit.edu
Thomas Fossati
Arm Limited
Thomas.Fossati@arm.com
Vincent Scarlata Intel
vincent.r.scarlata@intel.com

## Slide 2
Remote Attestation in a Heterogenous World
Confidential compute in an umbrella term
  Confidentiality of Code & Data
  Integrity of Code & Data
  Identity of Code
  Confidentiality of Execution
Support varies by chip type
Attested
Environment
Opaque clusters of networked TEE
  Secured meshes will span from Local Host through Cloud
  Attest security posture & peer identity
  Mesh a mix and match of TEE types across L1 ↔ L7 platforms
(and implicitly all of them)
Application
I trust you
attestation

## Slide 3: Categorizing Confidential Compute Protections
Process
Guest VM
Chip can’t lie about security measurements
Value proposition
TPM2
Application Data
VM Manager
Host OS
Cryptoprocessor
Attester
VM operates as a Walled Garden
SEV, TDX, ACCA, SEV-SNP
Guest VM
Host root admin or
privileged process
VM orchestration
Peer guest VM
Each process runs and saves opaquely
SGX, TrustZone
Process
Guest VM Operator or
privileged process
Process can’t expose unencrypted objects
Homomorphic Encryption
(future?)
Application developer
Protect visibility from rogue

## Slide 4: Trustworthy Assertions about an Attester
What can be trusted |  | 
Identity | Software | developer-instance
 |  | build-instance
 | Hardware | attesting-hw-type
 |  | attesting-hw-instance
 | Hardware | hw-instance-recognized
 |  | hw-instance-unknown
Integrity | Hardware | hw-authentic
 |  | hw-verification-fail
 | Files | executables-verified
 |  | executables-refuted
 |  | file-system-anomaly
 |  | source-data-integrity
 | Config | config-secure
 |  | config-insecure
 | Runtime | isolation
Confidentiality | Data | runtime-confidential
 |  | secure-storage
Actionable
Trustworthiness Appraisals about the instance
(with verifiable Freshness)
A verifiable
Identity instance related to the peer

## Slide 5: Build upon IETF’s draft-ietf-rats-architecture
+------------+
| | Compare Evidence
| Verifier | against appraisal policy
| |
+------------+
^ |
Evidence | | Attestation
| | Result
| v
+------------+ +-------------+
| |------------->| | Compare Attestation
| Attester | Attestation | Relying | Result against
| | Result | Party | appraisal policy
+------------+ +-------------+
Figure 5: Passport Model

## Slide 6: Build upon IETF’s draft-ietf-rats-architecture
Attester
Verifier A
Attesting Environment
Evidence
Attestation Results
Verifier
Signature
hw-authentic
secure-storage
runtime-confidential
build-instance
Evidence time
executables-verified
Relying Party (Verifier B)
Identity
is Verifier known & trusted ?
is Attester on Accept-List ?
Trust Appraisal
meets Trustworthiness ?
Freshness
is appraisal recent ?
Relying Party Freshness
Attesting
Environment
Signature
Relying Party fresh
Attestation Result Augmented Evidence
Verifier
Signature
hw-authentic
secure-storage
runtime-confidential
build-instance
Evidence time
executables-verified

## Slide 7: Normalizing Trustworthiness Claims
Appraisal of: |  | Trustworthiness Claim | Supportable Protection Technologies |  | 
Appraisal of: |  | Trustworthiness Claim | Process | Guest VM | Cryptoprocessor
Identity | Hardware | hw-instance-recognized | Optional | Optional | Optional
 |  | hw-instance-unknown | Optional | Optional | Optional
Integrity | Hardware | hw-authentic | Implicit | tbd | If PCR check ok
 |  | hw-verification-fail | Implicit if not ok | tbd | If PCR don't check ok
 | Files | executables-verified | Optional | Optional | If PCR check ok
 |  | executables-refuted | Optional | Optional | If PCR don't check ok
 |  | file-system-anomaly | n/a? | Optional | Insufficient
 |  | source-data-integrity | Optional | Optional | Optional
 | Config | config-secure | Optional | Optional | Optional
 |  | config-insecure | Optional | Optional | Optional
 | Runtime | isolation | Implicit | Implicit | Insufficient
Confidentiality | Data | runtime-confidential | Implicit | Insufficient (?) | Insufficient
 |  | secure-storage | Implicit | tbd | Very minimal space

## Slide 9: Trustworthiness Appraisal
Time
Boot
Time
Time
One to Many Trustworthiness Claims assigned during an appraisal cycle.
appraisal
config-secure
executables-verified
file-system-anomaly
hw-authentic
hw-verification-fail
config-secure
executables-verified
hw-authentic
Attester
Verifier

## Slide 10: Trusted Path Routing draft-voit-rats-trustworthy-path-routing
Verifier
Operational instance of draft-voit-rats-attestation-results
Network trust is established via each peer’s Link Layer credentials
Signed Appraisal returned to Router
passed to peers over EAP / TLS / 802.1x

## Slide 11: Example Trustworthiness Vector State Machine
Setting each Trustworthiness Claim is explicit.
It is possible to not assert ANY conclusions after the appraisal.
executables-verified
config-secure
hw-instance-recognized
PCR Quote received
Timer Expiry
Log received
Event
hw-verification-fail
config-insecure
Fail
Insufficient Data
Not Evaluated
Pass
Next Step
Push Trustworthiness Claim into Trustworthiness Vector
Legend
hw-authentic
hw-instance-unknown
executables-fail
Vector = Null
Fresh signed Evidence?
Evaluate HW Integrity
Evaluate Identity
Evaluate Boot Integrity
Evaluate config
Send Vector to
Attester