## Slide 1: Attestation Results for Secure Interactions
Eric Voit
Cisco
evoit@cisco.com
draft-voit-rats-attestation-results
Henk Birkholz Fraunhofer SIT
henk.birkholz@sit.fraunhofer.de
Thomas Hardjono
MIT
hardjono@mit.edu
Thomas Fossati
Arm Limited
Thomas.Fossati@arm.com
Vincent Scarlata Intel
vincent.r.scarlata@intel.com

## Slide 2
In the end, the trust we place in our digital infrastructure should be proportional to how trustworthy and transparent that infrastructure is.

## Slide 3
Remote Attestation in a Heterogenous World
Confidential compute in an umbrella term
  Confidentiality of Code & Data
  Integrity of Code & Data
  Identity of Code
  Confidentiality of Execution
Support varies by chip type
Attesting
Environment
Opaque clusters of networked TEE
  Secured meshes will span from Local Host through Cloud
  Attest security posture & peer identity
  Mesh a mix and match of TEE types across L1 ↔ L7 platforms
(and implicitly all of them)
Application
I trust you
attestation

## Slide 4: Categorizing Confidential Compute
CPU
Process
Guest VM
(or container)
Value proposition
Application Data
VM Manager
Host OS
Host root admin or
privileged process
VM orchestration
Peer guest VM
Guest VM
(or container)
Guest VM Operator or
privileged process
can’t lie about security measurements
TPM2
Hardware Security Module (HSM)
Deny visibility to rogue
VM operates as a Walled Garden
SEV, TDX, ACCA, SEV-SNP
Each process runs and saves opaquely
SGX, TrustZone
Process
Process can’t expose unencrypted objects
Homomorphic Encryption
(future?)
Application developer
Attester

## Slide 5: Built upon IETF’s draft-ietf-rats-architecture
+------------+
| | Compare Evidence
| Verifier | against appraisal policy
| |
+------------+
^ |
Evidence | | Attestation
| | Result
| v
+------------+ +-------------+
| |------------->| | Compare Attestation
| Attester | Attestation | Relying | Result against
| | Result | Party | appraisal policy
+------------+ +-------------+
Passport Model

## Slide 6: Built upon IETF’s draft-ietf-rats-architecture
Attester
Verifier A
Evidence
Attestation Result (AR)
Verifier
Signature
hw-authentic
secure-storage
runtime-confidential
target environment
timestamp
executables-verified
Relying Party (Verifier B)
Identity
is Verifier A known & trusted ?
is Attester on Accept-List ?
Trustworthiness Claims
what did Verifier A conclude ?
Freshness
is this Evidence recent ?
AR Augmented Evidence
hw-authentic
secure-storage
runtime-confidential
target environment
timestamp
executables-verified
Attesting
Environment
Signature
target environment
Attesting Environment
nonce
Attesting
Environment
Signature
nonce
Verifier
Signature

## Slide 7: Attestation Results Augmented Evidence a.k.a.: Things which the Relying Party might Action
Identity | Attesting Environment | ae-instance-recognized
 |  | ae-instance-unknown
Integrity | Hardware | hw-authentic
 |  | hw-verification-fail
 | Files | executables-verified
 |  | executables-refuted
 |  | file-system-anomaly
 |  | source-data-integrity
 | Config | config-secure
 |  | config-insecure
Confidentiality | Target Environment | target-isolation
 |  | runtime-confidential
 | Data | secure-storage
Trustworthiness Claims of the Verifier
Verified Identity instance(s)
Attester | chip vendor
 | chip type
 | target environment
Software Bill of Materials | target developer
 | ae instance
Verifier | verifier id
Verifiable Freshness
Random Number | nonce
Synchronized Clocks | timestamp
 | tuda sync token
Epoch | epoch id
+
+
hw-authentic
secure-storage
runtime-confidential
target environment
timestamp
executables-verified
Attesting
Environment
Signature
nonce
Verifier
Signature

## Slide 8: Normalizing Trustworthiness Claims
Trustworthiness Claim | Supportable Protection Technologies |  | 
Trustworthiness Claim | Process-based | VM-based | HSM-based
ae-instance-recognized | Optional | Optional | Optional
ae-instance-unknown | Optional | Optional | Optional
hw-authentic | Implicit | Chip dependent | If PCR check ok
hw-verification-fail | Implicit if not ok | Chip dependent | If PCR don't check ok
executables-verified | Optional | Optional | If PCR check ok
executables-refuted | Optional | Optional | If PCR don't check ok
file-system-anomaly | n/a | Optional | Insufficient
source-data-integrity | Optional | Optional | Optional
config-secure | Optional | Optional | Optional
config-insecure | Optional | Optional | Optional
target-isolation | Implicit | Implicit | Optional
runtime-confidential | Implicit | Implicit | Insufficient
secure-storage | Implicit | Chip dependent | Very minimal space

## Slide 9
Notes: Slide background color #0e284d

## Slide 10: Trustworthiness Appraisal
Time
Boot
Time
Time
One to Many Trustworthiness Claims assigned during an appraisal cycle.
appraisal
config-secure
executables-verified
file-system-anomaly
hw-authentic
hw-verification-fail
config-secure
executables-verified
hw-authentic
Attester
Verifier

## Slide 11: Trusted Path Routing draft-voit-rats-trustworthy-path-routing
Verifier
Operational instance of draft-voit-rats-attestation-results
Network trust is established via each peer’s Link Layer credentials
Signed Appraisal returned to Router
passed to peers over EAP / TLS / 802.1x

## Slide 12: Example Trustworthiness Vector State Machine
Setting each Trustworthiness Claim is explicit.
It is possible to not assert ANY conclusions after the appraisal.
executables-verified
config-secure
ae-instance-recognized
PCR Quote received
Timer Expiry
Log received
Event
hw-verification-fail
config-insecure
Fail
Insufficient Data
Not Evaluated
Pass
Next Step
Push Trustworthiness Claim into Trustworthiness Vector
Legend
hw-authentic
ae-instance-unknown
executables-fail
Vector = Null
Fresh signed Evidence?
Evaluate HW Integrity
Evaluate Identity
Evaluate Boot Integrity
Evaluate config
Send Vector to
Attester